## Slide 1: Automated Troubleshooting
Because work is for suckers.
Pete Lumbis – CCIE #28677, CCDE 2012::3 @PeteCCDE

## Slide 2: $whoami
Network Engineer
SE/Datacenter Architect at Cumulus Networks
5 years in Cisco TAC, Routing Escalation
CCIE, CCDE

## Slide 3: Change Management
Design
Implement
Troubleshoot

## Slide 4: Reality
Troubleshoot
Change
Upgrade
Because Tuesday

## Slide 5: Our Lives

## Slide 6: Troubleshooting like a Support Engineer
When did the problem start?
Rely on data, not socialization or opinions.
What evidence do we have?
Has this ever worked?
What are the requirements for this to work?

## Slide 7: On Evidence
Observable. Facts.

## Slide 8: An Example: New BGP Peer
When did the problem start?
  New Config
Rely on data, not socialization or opinions
  Show outputs indicate peer isn’t up
What evidence to do we have?
  The show commands
Has this ever worked?
  Nope
What are requirements for this to work?
  Coordinated ASNs, IPs. TCP connectivity

## Slide 9: Requirements of a New BGP Peer
Peer IPs coordinate
  Who is .1 and who is .2?
Peer ASNs coordinate
  Am I expecting the correct ASN that my peer has configured?
TCP/IP Connectivity
  Ping?
  Telnet on port 179?

## Slide 10: Troubleshooting a BGP Peer
Stare and Compare
Ping
Telnet
Debugs, maybe?

## Slide 11: Stare and Compare Works
leaf01: router bgp 65001
bgp router-id 10.1.1.1
neighbor 172.16.255.2 remote-as 65531
spine01: router bgp 65531
bgp router-id 10.100.100.1
neighbor 172.16.255.1 remote-as 65001

## Slide 12: Until It Doesn’t Work
cumulus@leaf01:~$ net show interface swp51
Name MAC Speed MTU Mode
-- ------------------ ----------------- ------- ----- ------------
UP swp51 (to Spine01) 44:38:39:00:00:5b 1G 1500 Interface/L3
IP Details
------------------------- ---------------
IP: 172.16.255.1/31
IP Neighbor(ARP) Entries: 0
LLDP
------ ---- -------------
swp51 ==== swp1(spine01)

## Slide 13: Until It Doesn’t Work
cumulus@leaf01:~$ net show interface swp51
Name MAC Speed MTU Mode
-- ------------------ ----------------- ------- ----- ------------
UP swp51 (to Spine01) 44:38:39:00:00:5b 1G 1500 Interface/L3
IP Details
------------------------- ---------------
IP: 172.16.255.1/31
IP Neighbor(ARP) Entries: 0
LLDP
------ ---- -------------
swp51 ==== swp1(spine01)
router bgp 65001
bgp router-id 10.1.1.1
neighbor 172.16.255.2 remote-as 65531

## Slide 14: Until It Doesn’t Work
cumulus@leaf01:~$ net show interface swp51
Name MAC Speed MTU Mode
-- ------------------ ----------------- ------- ----- ------------
UP swp51 (to Spine01) 44:38:39:00:00:5b 1G 1500 Interface/L3
IP Details
------------------------- ---------------
IP: 172.16.255.1/31
IP Neighbor(ARP) Entries: 0
LLDP
------ ---- -------------
swp51 ==== swp1(spine01)
router bgp 65001
bgp router-id 10.1.1.1
neighbor 172.16.255.2 remote-as 65531
/31 Mask!

## Slide 15: Until It Doesn’t Work
cumulus@leaf01:~$ net show interface swp51
Name MAC Speed MTU Mode
-- ------------------ ----------------- ------- ----- ------------
UP swp51 (to Spine01) 44:38:39:00:00:5b 1G 1500 Interface/L3
IP Details
------------------------- ---------------
IP: 172.16.255.1/31
IP Neighbor(ARP) Entries: 0
LLDP
------ ---- -------------
swp51 ==== swp1(spine01)
router bgp 65001
bgp router-id 10.1.1.1
neighbor 172.16.255.2 remote-as 65531
/31 Mask!
Wrong Subnet

## Slide 16: That Feeling….

## Slide 17: Troubleshooting Flowcharts

## Slide 18: Human Error
Observable Data, only as good as the observer
Remove the human

## Slide 19: Flowcharts Make Good Programs
If State == Init
  Check network type
  Check OSPF Authentication
  Check L1/L2 connectivity
Else
  Escalate

## Slide 20: What’s Changed?
APIs, et al.
Abstracting hard stuff
  Ansible handles SSH, authentication, etc
  REST is easy to use

## Slide 21: Let’s Try It!

## Slide 22: The Goal
Settle for less
Hard/Impossible to automate everything
Automate most
Jumpstart manual troubleshooting
Push-button Tier 1 Support

## Slide 23
Questions?
https://github.com/plumbis/interop17-troubleshooting